| Company Name: Site: |  | COSHH Assessment |
| --- | --- | --- |
| Supplier: | CORROLESS EPF BLACK TEMPERATE HARDENER | COSHH Number | 29 |
|  |  | page 1 |
| Assessment By: | Activity: Preparation to paint | Review Date | Assessment Date |
| Northern Counties Safety Group. | Roller or brush of application of rust protector |  |  |
|  | Persons/Groups at Risk |  |  |
|  | Site operatives /other contractors. |  |  |

NAME OF HAZARDOUS SUBSTANCE USED OR CREATED

Substance: Activator for 2 Component System

| FLAMMABLE |  | TOXIC |  | IRRITANT |  | OXIDISING |  | HARMFUL |  | CORROSIVE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |
| ( |  |  |  | ( |  | ( |  |  |  | ( |  | ( |  |  |  | ( |
| Insert ( in appropriate boxes |

| Please add comments into boxes where required. | Insert ( in appropriate boxes and add comment below | YES | NO |
| --- | --- | --- | --- |
| Is Manufacturers Safety Data Sheet available? |  | ( |  |
| Does the Substance have a Workplace Exposure Limit (WEL)? | Xylene, mixture of isomers- 50.000 - 8hr TWA 100.000- 15 Min STEL Crystalline silica- 0.10m-TWA | ( |  |
| If the substance has a WEL please state. if un-sure check HSE document – EH40 |  | ( |  |
| Can a safer substance be used or can the substance be enclosed or extracted. |  |  | ( |
| Will employees be given information and training? |  | ( |  |
| Will Personal Protective Equipment be provided for employees? |  |
| State the standard of RPE (respirators) | P3 Cartridge organic vapour FFP3 Disposable organic vapour respirator | ( |  |
| State the standard of Goggles or Spectacles | BS679 Goggles | ( |  |
| State the standard of Gloves | Nitrile /Pvc gloves to be worn | ( |  |
| State the standard of Overalls |  | ( |  |
| State the standard of Boots |  | ( |  |
| Other Equipment | Attach details if YES |  |  |
| Will Exposure Monitoring and/or Control Measures be required? | Attach details if YES |  | ( |
| Will Health Surveillance be necessary? | Attach details if YES | ( |  |
| Does this Substance need to be disposed of by a Waste Disposal Contractor? | ( |  |
| Have all necessary First-aid and welfare requirements been provided? |  | ( |  |
| Have Storage requirements for the substance been provided / arranged on site? |  | ( |  |
| FIRST AID, FIRE FIGHTING, STORAGE & HANDLING, DISPOSAL AND ACCIDENTAL RELEASE INSTRUCTIONS ARE PROVIDED ON PAGES 2 & 3 | Number of Sheets attached to this Assessment |  |
| FIRST AID INSTRUCTIONS |
| Route of Exposure, or Type of Injury | First Aid Treatment |
| Skin Contact | Remove contaminated clothing. Wash skin thoroughly with soap and water or recognised skin cleaner. Do NOT use solvents or thinners |
| Eye Contact | Immediately irrigate copiously with clean water for at least 10 minutes |
| Inhalation | Remove to fresh air if breathing is irregular or stopped administer artificial respiration. |
| Ingestion | If swallowed obtain immediate medical attention. Keep at rest. Do NOT induce vomiting |
| General Information | In all cases of doubt, or when symptoms persist, seek medical attention. * If unconscious place in recovery position, give nothing by mouth. |

| FIRE FIGHTING MEASURES |
| --- |
| Hazard | Measures |
| Fire | Extinguishing Media: alcohol resistant foam, CO2, powder or water fog. Never use water jets or water from buckets etc. to fight fire. |
| Stability | Stable under recommended storage and handling conditions. Decomposition products are carbon monoxide , carbon dioxide, smoke and Oxides of nitrogen. Keep away from oxidising agents, alkali and acid. . |
| Decomposition Products |  |

| MANUFACTURERS INFORMATION |
| --- |
| Manufacturers Name and Address | CORROLESS Corrosion Control Kelvin Way, West Bromwich West Midlands B70 7JZ |
| Manufacturers Health & Safety Data Sheet Reference |  |
| 24 Hour Emergency Telephone Number | (0121) 525 5665 |
| Regulatory Information: Warning Label Phrases | R48/20 Harmful:danger of serious damage to health by prolonged exposure through inhalation R43 May cause sensitisation by skin contact R36/38 Irritating to the eyes and skin S23c Do not breathe vapour or spray mist S26 In case of contact with eyes, rinse immediately with plenty of water and seek medical advice S42 During spraying suitable respiratory equipment S7/9 Keep container tightly closed and in a well ventilated place S24 Avoid contact with skin |

| STORAGE AND HANDLING |
| --- |
| Hazard | Measures |
| Handling | Persons with history of skin sensitisation problems should be monitored. Where this product is used unless under appropriate medical supervision. * Keep the container tightly closed. * Avoid skin and eye contact/inhalation of mist. * Guide pack weight:[5 Ltr= 10 Kgs] [20 Ltr= 37 Kgs] [25 Ltr= 46 Kgs] |
| Storage | Observe the label precautions. Separate from oxidising agents |

| DISPOSAL MEASURES |
| --- |
| Hazard | Measures |
| Pollution of water courses or drains | In accordance with Control of Pollution Act and Environmental Protection Act |

| ACCIDENTAL RELEASE MEASURES |
| --- |
| Hazard | Measures |
| Spillage | Exclude sources of ignition. * Ventilate the area. * Exclude non-essential personnel. * Avoid breathing vapours. * Contain/collect spillage with non-combustible absorbent materials. |

| USAGE/EXPOSURE |
| --- |
| Frequency and Duration of use | Daily |
| Maximum number of people involved in activity | 30 employees |
| Quantities stored/used | 5 litres |

1. Ensure the specified PPE is worn when handling

2. Respirators to be worn at all times whilst applying the paint.

3. Remove any sheeting where practicable when working from sheeted scaffold, to increase airflow

4 If adequate airflow cannot be maintained atmospheric monitoring required.

5. Provide adequate ventilation at all times.

6. Health surveillance to be carried out on a yearly basis through the use of an occupational professional to monitor for skin sensitisation such as dermatitis as well as cross sensitisation to other epoxies .

7. Keep containers closed at all times whilst not in use, to eliminate vapour release.

8. Persons with a history of asthma, allergies chronic or recurrent respiratory disease should only work with this product under appropriate medical supervision.

| Name: | Signature: | Date: | Name: | Signature: | Date: |
| --- | --- | --- | --- | --- | --- |

# Text boxes

Safe System of Work

Operatives Acknowledgement