| Company Name: Site: |  | COSHH Assessment |
| --- | --- | --- |
| Supplier: | LG-Chem.Ltd | COSHH Number | 50 |
|  |  | page 1 |
| Assessment By: | Activity: | Review Date | Assessment Date |
|  | Construction usage including cutting, sanding and drilling.routering |  |  |
|  | Persons/Groups at Risk |  |  |
|  | Joiner, Site Operative/User of product |  |  |

NAME OF HAZARDOUS SUBSTANCE USED OR CREATED

Substance: LG HI-MACS

| FLAMMABLE |  | TOXIC |  | IRRITANT |  | OXIDISING |  | HARMFUL |  | CORROSIVE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |
|  | ( |  |  | ( |  |  | ( |  |  | ( |  |  | ( |  |  | ( |
| Insert ( in appropriate boxes |

|  | Insert ( in appropriate boxes and add comment below | YES | NO |
| --- | --- | --- | --- |
| Is Manufacturers Safety Data Sheet available? |  | ( |  |
| Does the Substance have a Workplace Exposure Limit (WEL)? |  | ( |  |
| If the substance has a WEL please state. if un-sure check HSE document – EH40 | Inhalable dust 15 mg/m3 per 8 hour | ( |  |
| Can a safer substance be used or can the substance be enclosed or extracted. |  |  | ( |
| Will employees be given information and training? |  | ( |  |
| Will Personal Protective Equipment be provided for employees? |  |
| State the standard of RPE (respirators) | Minimum standard of FFP2. | ( |  |
| State the standard of Goggles or Spectacles | BSEN166 as a nuisance inhibitor | ( |  |
| State the standard of Gloves |  |  | ( |
| State the standard of Overalls |  |  | ( |
| State the standard of Boots |  | ( |  |
| Other Equipment | Attach details if YES |  | ( |
| Will Exposure Monitoring and/or Control Measures be required? | Attach details if YES | ( |  |
| Will Health Surveillance be necessary? | Attach details if YES | ( |  |
| Does this Substance need to be disposed of by a Waste Disposal Contractor? | ( |  |
| Have all necessary First-aid and welfare requirements been provided? |  | ( |  |
| Have Storage requirements for the substance been provided / arranged on site? |  | ( |  |
| FIRST AID, FIRE FIGHTING, STORAGE & HANDLING, DISPOSAL AND ACCIDENTAL RELEASE INSTRUCTIONS ARE PROVIDED ON PAGES 2 & 3 if required | Number of Sheets attached to this Assessment |  |
| FIRST AID INSTRUCTIONS |
| Route of Exposure, or Type of Injury | First Aid Treatment |
| Skin Contact | In case of irritation from dust generated from processing of Hi-macs, wash with water. |
| Eye Contact | If particles enter the eyes during processing, immediately flush eyes with plenty of water. Seek medical attention if irritation persists. |
| Inhalation | Inhalation of Himacs dust can only occur during processing. If inhalation of dust causes adverse effects, remove to fresh air. If discomfort persists, seek medical advice. |
| Ingestion | If ingestion occurs seek immediate medical attention. Wash out mouth with clean water where appropriate |
| General Information | Ensure that the stated PPE is worn and all staff are informed of the risks, control measures and precautions required when working with the substance. |

| FIRE FIGHTING MEASURES |
| --- |
| Hazard | Measures |
| Fire | Non-flammable in presence of shocks, heat, oxidizing materials, reducing materials combustible materials, organic materials, metals, acids, alkalis, moisture. Use DRY chemicals,CO2, water spray or foam. |
| Stability | N/A |
| Decomposition Products | Some metallic oxides |

| MANUFACTURERS INFORMATION |
| --- |
| Manufacturers Name and Address | Chemical Product and Company Identification LG-Chem.LTD 20 Yoido-Dong, Youngdungpo-Gu Seoul 150-721, Korea Tel.: 82 (0)2 3773 7760 Fax: 82 (0)2 3773 7972 |
| Manufacturers Health & Safety Data Sheet Reference | N/A |
| 24 Hour Emergency Telephone Number | 82 (0) 237737760 |
| Regulatory Information: Warning Label Phrases | None attributable |

| STORAGE AND HANDLING |
| --- |
| Hazard | Measures |
| Handling | Do not breathe dust. If user operations generate dust, use ventilation to keep exposure airborne contaminates below the exposure limit. |
| Storage | No specific storage is required. Be sure that it is not necessary to strain to reach materials, and that shelves are not overloaded. |

| DISPOSAL MEASURES |
| --- |
| Hazard | Measures |
| Disposal of collected dusts from Local Exhaust Ventilation or from vacuums. | This may expose the operative to higher concentrations of the dusts therefore; a minimum standard of FFP2 masks are advised. Dusts must be kept contained during disposal and subsequent storage. Disposal to landfill etc must be by a registered carrier. |

| ACCIDENTAL RELEASE MEASURES |
| --- |
| Hazard | Measures |
|  | LG HI- MACS does not represent a hazard in sheet form. However dust generated from processing LG HI –MACS should be contained carefully collected and removed. |

| USAGE/EXPOSURE |
| --- |
| Frequency and Duration of use |  |
| Maximum number of people involved in activity |  |
| Quantities stored/used |  |
| Exposure levels | Health: The following health problems are among the effects that have been associated with exposure to LG HI-MACS dust. Cuts of sharp edges Obstruction in the nose and rhinitis; Dust generated during fabrication may irritate eyes a) Exposure Controls: During processing, adequate ventilation and/ or extraction should be provided to minimise airborne dust. Whenever possible, fit dust extraction equipment even when using hand-held machines. b) Personal Protection: Dust will be created during processing; use appropriate (Dust masks to at least EN 149 type FFP2) respiratory Protection equipment. Wear gloves and overalls as required to prevent skin contact. Wear eye protection to prevent dust particles from entering eyes. Wear the correct clothing and use other safety equipment as necessary. |

- Ensure that adherence to this COSHH Risk Assessment is adhered to at all times.

- Wash at the end of each work shift and before eating, smoking and using the toilet.

- When machining ensure on-tool extraction is fitted and working and all LEV is fully functional.

N.B.  Airborne dust monitoring has indicated that WEL has not been exceeded.

Low level health surveillance is in place in the form of annual health questionnaires.

| Name: | Signature: | Date: | Name: | Signature: | Date: |
| --- | --- | --- | --- | --- | --- |

# Text boxes

Safe System of Work

Operatives Acknowledgement   LG Himacs