| Company Name: Site: |  | COSHH Assessment |
| --- | --- | --- |
| Supplier: | Sovereign Chemicals Ltd | COSHH Number | 53 |
|  |  | page 1 |
| Assessment By: | Activity: | Review Date | Assessment Date |
|  | Using a spreader and or brush to apply contact adhesive to wood edging and faces |  |  |
|  | Persons/Groups at Risk |  |  |
|  | Joiner Shop Operative/User of product |  |  |

NAME OF HAZARDOUS SUBSTANCE USED OR CREATED

Substance: Sovereign Contact Adhesive

| FLAMMABLE |  | TOXIC |  | IRRITANT |  | OXIDISING |  | HARMFUL |  | CORROSIVE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |
| ( |  |  | ( |  |  | ( |  |  |  | ( |  | ( |  |  |  | ( |
| Insert ( in appropriate boxes |

|  | Insert ( in appropriate boxes and add comment below | YES | NO |
| --- | --- | --- | --- |
| Is Manufacturers Safety Data Sheet available? |  | ( |  |
| Does the Substance have a Workplace Exposure Limit (WEL)? |  | ( |  |
| If the substance has a WEL please state. if un-sure check HSE document – EH40 | See safety data sheet | ( |  |
| Can a safer substance be used or can the substance be enclosed or extracted. |  |  | ( |
| Will employees be given information and training? |  | ( |  |
| Will Personal Protective Equipment be provided for employees? | ( |
| State the standard of RPE (respirators) | Cartridge mask to en140 A1 if adequate ventilation not available | ( |  |
| State the standard of Goggles or Spectacles | BSEN166 goggles | ( |  |
| State the standard of Gloves | Nitrile | ( |  |
| State the standard of Overalls |  |  | ( |
| State the standard of Boots |  |  |  |
| Other Equipment | Attach details if YES |  | ( |
| Will Exposure Monitoring and/or Control Measures be required? | Attach details if YES |  | ( |
| Will Health Surveillance be necessary? | Attach details if YES |  | ( |
| Does this Substance need to be disposed of by a Waste Disposal Contractor? | ( |  |
| Have all necessary First-aid and welfare requirements been provided? |  | ( |  |
| Have Storage requirements for the substance been provided / arranged on site? |  | ( |  |
| FIRST AID, FIRE FIGHTING, STORAGE & HANDLING, DISPOSAL AND ACCIDENTAL RELEASE INSTRUCTIONS ARE PROVIDED ON PAGES 2 & 3 if required | Number of Sheets attached to this Assessment |  |
| FIRST AID INSTRUCTIONS |
| Route of Exposure, or Type of Injury | First Aid Treatment |
| Skin Contact | Wipe off excess with a paper towel and then clean with resin removing cream or hand cleanser. Do not use solvents. Finally wash with soap and water. |
| Eye Contact | Wash with copious amounts of water for at least 15 minutes. Obtain medical attention. |
| Inhalation | Remove affected person from source of exposure. Remove exposed person to fresh air at once. Keep patient warm and at rest. Obtain medical assistance. |
| Ingestion | Do not induce vomiting. Obtain immediate medical attention. |
| General Information | Where risk of splashing occurs, wear splash proof goggles, wear gloves and appropriate clothing to prevent repeated and prolonged skin contact. If ventilation is not adequate, wear respiratory protection conforming to EN 140 with A1 filters. |

| FIRE FIGHTING MEASURES |
| --- |
| Hazard | Measures |
| Fire | Fire may be extinguished using Powder, Foam or CO2. Contact Adhesive vapours will form explosive mixtures with air. Being heavier than air, vapours will concentrate and may travel for considerable distances along the ground, down stairways etc. This extends the fire and explosion hazard beyond the immediate vicinity of the workplace. Use sand or earth for containment if there is a danger of spreading or flowing. Not to be used near naked flames, sparks or hot surfaces. Do not smoke. Eliminate all sources of ignition and avoid build up of static electricity by earthing plant etc. Do not pour adhesive from plastic containers. |
| Stability |  |
| Decomposition Products | Toxic gases/vapours/fumes of: Carbon Dioxide (CO2) Carbon Monoxide (CO). |

| MANUFACTURERS INFORMATION |
| --- |
| Manufacturers Name and Address | Sovereign Chemicals Limited Park Road Barrow-in-Furness Cumbria, LA14 4EQ |
| Manufacturers Health & Safety Data Sheet Reference | SDS 023 |
| 24 Hour Emergency Telephone Number | 01229 870800 – Office Hours 01785 272650 – Out of Hours |
| Regulatory Information: Warning Label Phrases | R11 Highly flammable R20 Harmful by inhalation R38 Irritating to skin R51/53 Toxic to aquatic organisms, may cause long-term adverse effects in the aquatic environment R65 Harmful: may cause lung damage if swallowed |

| STORAGE AND HANDLING |
| --- |
| Hazard | Measures |
| Handling | Avoid spilling, skin and eye contact. Ventilate well, avoid using vapours. Used approved respirator. |
| Storage | Flammable/combustible – keep away from oxidisers, heat and flames. Earth container and transfer equipment to eliminate static electric sparks. Keep away from heat, sparks and open flame. Use and store in accordance with the Highly Flammable Liquids & Liquefied Petroleum Gases Regulations 1972. |

| DISPOSAL MEASURES |
| --- |
| Hazard | Measures |
|  | Dispose of as Special Waste in accordance with Local Authority Regulations. Use only licensed waste hauliers and disposal contractors. |

| ACCIDENTAL RELEASE MEASURES |
| --- |
| Hazard | Measures |
|  | Ensure all possible sources of ignition are removed and supply adequate ventilation. Wear appropriate PPE. Confine major spillages using an inert non-combustible material to restrict spread of adhesive and contamination of drainage systems and waterways. Restrict continued evaporation of vapours with a blanket of foam. Soak up with inert absorbent (eg. Sand). Pick up with spark proof tools and place impregnated absorbent in sealed adequately labelled metal containers pending safe disposal. |

| USAGE/EXPOSURE |
| --- |
| Frequency and Duration of use |  |
| Maximum number of people involved in activity |  |
| Quantities stored/used |  |
| Exposure levels | Health: Wear splash proof goggles conforming to BSEN 166 to avoid any possibility of eye contact. Use CE approved nitrile protective gloves. Wear appropriate clothing to prevent repeated or prolonged skin contact. a) Exposure Controls: If ventilation is not adequate, wear respiratory protection conforming to EN 140 with A1 filters. |

- Ensure that adherence to this COSHH Risk Assessment is adhered to at all times.

- Wash at the end of each work shift and before eating, smoking and using the toilet.

- When using Contact Adhesive in confined areas ensure adequate ventilation.

Low level health surveillance is in place in the form of annual health questionnaire.

| Name: | Signature: | Date: | Name: | Signature: | Date: |
| --- | --- | --- | --- | --- | --- |

# Text boxes

Safe System of Work

Operatives Acknowledgement