| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Planning refurbishment/minor demolition work on buildings that may contain asbestos containing materials (ACM’s) |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Planning of refurbishment/demolition work | Inadvertent exposure to asbestos due to not being aware of its presence during work in premises | Workers, client’s personnel, general public, young/old/infirm, visitors | H | Consult the asbestos register, made to record the results of the survey carried out to comply with regulation 4 of the Control of Asbestos Regulations 2012 (CAR) to determine whether asbestos that could present a risk during the work is present and if so the type of asbestos. If there is no register, do not commence work until the survey has been carried out. A refurbishment/demolition survey (type 3) must be carried out on any areas where the fabric of the building is to be disturbed (i.e. creating new window/door openings, removing stud walls etc.). Where there is only a management survey for the building (Type 2). This is not sufficient for refurbishment/demolition work. All operatives working on any refurbishment/demolition work MUST have attended a ½ day Asbestos Awareness training course. | M |

| Refurbishment/demolition work on or around asbestos-containing materials (ACMs) such as asbestos insulation, asbestos coating and asbestos insulation board which could result in the slightest release of asbestos fibres of any type | Inadvertent exposure to asbestos fibres | Workers, client’s personnel, general public, young/old/infirm, visitors | H | Specialist risk assessment to comply with the Control of Asbestos Regulations 2012 (CAR). Where work has to be carried out that will involve ACMs, it will have to be carried out by a contractor licensed under the Control of Asbestos Regulations 2012, unless: The exposure of employees to asbestos fibres during the work is sporadic and low intensity. It is clear from the risk assessment that the control limit (0.1 asbestos fibres per cm³ of air averaged over a continuous period of 4 hours) will not be exceeded The work involves: Short, non-continuous maintenance activities Removal of materials in which the asbestos fibres are firmly linked in a matrix, e.g. asbestos cement and asbestos containing textured decorative coatings such as Artex, vinyl floor tiles Encapsulation or sealing of asbestos –containing materials which are in good condition Air monitoring and control The collection and analysis of samples to ascertain whether a specific material contains asbestos. If in any doubt, consult Northern Counties Safety Group Safety Advisors for advice. | M |
| --- | --- | --- | --- | --- | --- |

| Work involving the removal of asbestos cement (AC) sheeting, materials in which the asbestos fibres are firmly linked in a matrix, e.g. asbestos cement and asbestos containing textured decorative coatings such as Artex, vinyl floor tiles | Inadvertent exposure to asbestos fibres | Workers, client’s personnel, general public, young/old/infirm, visitors | H | An individual, site specific risk assessment must be produced for any non-licensable, non-notifiable asbestos removal works. All operatives carrying out such work MUST have attended a 1 day non-licensable, non-notifiable, asbestos removal training course. If in any doubt, consult Northern Counties Safety Group Safety Advisors for advice. | M |
| --- | --- | --- | --- | --- | --- |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK