| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Use of Asphalt Paver |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Operation of Paver | Entrapment | Plant operators | H | Ensure all emergency stop buttons are working before use. Only competent and trained operators to drive paver. Only competent and trained persons to operate screed/side plate. Do not attempt to clear blockages when auger is operating. | L |
| Operation of Paver | Fire | Plant operators, Civils operatives | H | Ensure burner controls are functioning correctly prior to use. Check all gas hoses and connections for damage prior to use. Ensure fire extinguisher is in place before use. | L |
| Operation of Paver | Collision with pedestrians/other vehicles | Plant operators, Civils operatives, other contractors, visitors | M | Only competent and trained operators to drive paver. Operator to have appropriate driving licence to drive on public roads. Site/road speed limits to be adhered to at all times. Driver must have clear forward/rear field of vision at all times. | L |
| Operation of Paver | Unauthorised use | Plant operators, Civils operatives, other contractors, visitors | M | When not in use, paver must be parked with handbrake applied and keys removed in site compound or other secure area. | L |
| Operation of Paver | Noise | Plant operators, Civils operatives | M | 1. Operatives to wear hearing protection when paver is operating. | L |
| Operation of Paver | Interaction with public/traffic | Plant operators, Civils operatives, other contractors, visitors | M | Flashing beacons to be switched on at all times. Banksman to be in attendance when paver is in use. | L |

| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |
| --- | --- | --- | --- | --- | --- |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK