| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
| Description Of Work: | Hand Held Blower |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Hand Held Blower | Fuel and Ignition sources | Operator and other workers in the vicinity | H | Fuel is extremely flammable; therefore keep clear of naked flames and ignition sources. Do not spill any fuel and use spill kits to collect any spillages. Do not smoke and always switch off when refuelling. Do not refuel with a hot engine. | L |
|  | Work related upper limb disorders and manual handling | Operator | M | Weight of blower 4.2kg Always hold firmly onto the rear handle to control Use smooth actions during operations Report any muscle strains or back problems to the manager. Ensure clear area for good footing during operation to aid manual handling and reduce the trip risk. Ensure safe access to areas required. | L |
|  | Flying particles | Operator, other workers, client’s personnel. | H | Ensure eye protection is worn and heavy duty gloves Check area for cars and other equipment that could be damaged and report to manager if a hazard has been identified. Safety boots with steel toe caps to be worn. | L |
|  | Exhaust Fumes | Operator, other workers, client’s personnel. | H | The blower is designed for outdoor use only. Do not take indoors due to risk of fume build up. | L |
|  | Noise. | Operator, other workers, client’s personnel, general public, visitors. | M | Wearing of hearing protection when above 80dB(A) The noise levels for the blower are 104dB (A) Therefore hearing protection must be worn at all times by the operator. Consider audiometry / health surveillance testing for regular users who are exposed to above noise levels | L |
|  | Weather. | Operator | M | Wet weather gear to be worn if raining. However, preferred to delay works until poor weather clears. | L |
|  | Unauthorised use. | Operator, other workers, client’s personnel, general public, visitors. | M | Lock away blower when not in use. | L |
|  | Vibration | Operator | M | Equipment should be serviced and maintained to reduce vibration Worn parts will be reported immediately Reduce the period of exposure. Job rotation (sharing the work and vibration exposure between several people) Stagger work activities (breaks) to ensure that workers undertake non vibration exposure activities following vibration exposure. Assess vibration times with blower at 7m/s2 (1hour trigger time) Health surveillance programme of health checks to identify early signs and symptoms of hand arm vibration syndrome. Workers will be informed on the importance of maintaining blood circulation, keeping warm. Wet gloves must be removed and the welfare facilities will be warm and dry | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK