|  |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Use of 5/3 Cement Mixer |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
|  | Hazardous substances, mortar. | Operatives, bricklayers | H | Risk of dermatitis or cement burns and precautions explained to all workers. Use cement or cement containing products within the use-by date. Direct skin contact to be avoided, CE marked PVC gloves used when handling mortar. Good washing facilities on site, with hot and cold water, soap and basins large enough to wash forearms. Principal contractor’s first aid includes emergency eyewash. Training on how to treat exposure to be given to all operatives. Supervisor to be aware of anyone with early signs of dermatitis. | L |
|  | Hazardous substances, cement | Operatives, bricklayers | H | FFP3 dust masks to be worn when loading cement from bags into mixer Eye protection (goggles to BS EN166) to be worn CE marked PVC gloves used when handling cement. | L |
|  | Starting mixer | Operatives, bricklayers | H | If possible use electric 110v powered mixers If using diesel/petrol powered mixers, then electric start is preferable. If starting handle must be used, an anti-kickback type should be supplied. Keep thumbs parallel with the handle grip whilst winding. | L |
| Operating cement mixer. | Mixer falling over and entanglement | Operatives, bricklayers | H | Cement mixer located on firm, level ground Mixer is fully guarded and guards in place during operation. No loose clothing to be worn when operating mixer. Shovels must not be inserted into mixer when is is rotating. | L |
|  | Damage to electrics could result in a shock. | Operatives, bricklayers | H | Mixer is 110 volt and PAT tested every three months. Supervisor to check mixer daily for obvious damage. | L |
|  | Noise | Operatives, bricklayers | H | Hearing protection to be worn when operating diesel powered mixers. Electric mixers will not normally exceed noise exposure limits. | L |
|  | Fire when refuelling | Operatives, bricklayers | H | Ensure engine is stopped before refuelling. Ensure all naked flames and other sources of ignition are extinguished. Fuel to be stored in correct containers or tanks with bunds and drip trays | L |
|  | Welfare/first aid | Good facilities help prevent dermatitis etc. | H | Principal contractor will have facilities on site by the time bricklaying starts, including: Flushing toilet Hot and cold running water, soap, towels and full-size washbasins Heated canteen with kettle etc. First-aid equipment Principal contractor will arrange clearing and ensure the necessary electrical and heating safety checks are made and Site agent is appointed person for first aid. Supervisor to brief workers on facilities and keeping them clean. | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK