NORTHERN COUNTIES SAFETY GROUP LIMITED

Safety Training & Services to the Construction Industry

Only trained and authorized employees

to use this machine as per ACOP L114

Safe Use Procedures

- Cutting material to width using rip fence

- Cutting timber to length using the cross cut fence

- Cutting angles using approved guards

- A push stick MUST be available and used at all times

- Blade is to be sharp, of correct size, secure and correctly adjusted

- The gap between saw guard and top of component to be no more than 12mm

- The gap between the front edge of the riving knife and blade must be set as close as possible and within 8mm

- This machine must not be left running unattended

- Use braking devices at all times when stopping the machine

- Ensure the working area around the machine is kept clear at all times

- Correct use of Personal Protective Equipment at all times

- Use of correct Manual Handling techniques at all times

Machine Maintenance and Cleaning

- Employees must not clean the machine whilst still in motion

- Ensure that all maintenance is carried out following the machine manufacturer’s instructions

Limitations

- Rebating and grooving should be carried out on a Vertical Spindle Moulder

# Text boxes

Safe Use of Circular Saw