| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Installing partitions |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Dry Lining | Eyes | Employees, other workers, client’s personnel, visitors. | H | Wearing minimum of safety glasses for overhead work. | L |
|  | Dust/fibres | Employees, other workers, client’s personnel, visitors. | M | Provide natural ventilation. Wear gloves when handling insulation. Use vacuum cleaner instead of sweeping, wear suitable masks if sweeping. | L |
|  | Manual Handling | Employees, other workers, client’s personnel, visitors. | H | Utilise mechanical handling where possible. Provide training, install stairs early, deliver close to work area, provide assistance and trolleys. | L |
|  | Dermatitis | Employees, other workers, client’s personnel, visitors. | M | Use of barrier cream, wear goves and monitoring of skin condition. | L |
|  | Electricity | Employees, other workers, client’s personnel, visitors. | H | Inspection and maintenance of site electrical distribution and hand tools. In date PAT test. User inspection of tools, careful siting of leads, preference given to battery tools. Information on services buried in the wall. | L |
|  | Slips, trips and falls | Employees, other workers, client’s personnel, visitors. | H | Provision of waste skips and responsibility for daily cleaning Careful siting of cables. Use of purpose made hop ups or access equipment. Aluminium towers, scaffolds or MEWPS preferred means of access. Training for steps and ladders including ladder inspection. Work area cleared at the end of shift. | L |
|  | Nails | Employees, other workers, client’s personnel, visitors. | M | Removal of protruding nails. Safety footwear with midsoles to be worn. | L |
|  | Glass | Employees, other workers, client’s personnel, visitors. | M | Provision of suitable gloves during handling. Light eye protection Suction grips to be used for safe handling Separate manual handling assessment or add additional controls below for glass heavier than 20kg | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK