| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Use of portable electrical tools (except electrical chainsaws). |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Electrical Tools | Noise | Operator, other workers, clients personnel, general public, visitors | M | Enforce wearing of carefully selected ear defenders when noise above 85dB(A) Separate other workers and post ear protection zone signage. Job rotation to reduce personal noise and vibration exposure. Use low vibration, well maintained equipment, keep hands warm and avoid smoking. Provide health monitoring, ie audiometric testing, as required. | L |
|  | Injury from the toolbit | Operator, other workers, clients personnel, general public, visitors | M | Provision of training as required. User inspection and cleaning and manufacturers or hirers instruction book should be readily available and followed. Use clamps to secure workpiece where reasonably practicable. Wear eye protection. Disconnect from the supply when changing or adjusting the toollbit. Long hair should be tied back and loose clothing and jewellery removed. | L |
|  | Slips and falls while operating the tool | Operator, other workers, clients personnel, general public, young/old/infirm, visitors | H | Good lighting. Good housekeeping. Work area cleared of waste and unnecessary equipment. Work platforms, ie scaffolding or MEWPS to be used if necessary instead of ladders or steps. | L |
| Electrical Tools | Fire/explosion/electrocution | Operator, other workers, clients personnel, general public, visitors | H | Prohibit use of 240v equipment, where reasonably practicable use 110v or battery-operated tools (preferable for work at height). Regular maintenance and connection to a suitable protected and supervised supply carefully routed to avoid environmental hazards such as traffic. Prohibit use in explosive or flammable materials if tool ejects hot material eg sparks – consider hot work permit. Test and inspection PAT (every 3 months for 110v construction equipment), including user inspection of tools, leads and any transformers or distribution boxes. Tools to be earthed or doubled insulated. Supply to have emergency means of disconnection. Procedures for reporting damage and obtaining replacement tools. | L |
|  | Unauthorised use | Operator, other workers, clients personnel, general public, visitors | M | Issue tools only to competent persons and do not lone tools. | L |
|  | Dust, sparks, swarf | Operator, other workers, clients personnel, general public, visitors | H | Clear the working area of other people. Use a vacuum cleaner instead of sweeping; provide hoses and extraction units, wear, masks and goggles in accordance with any assessment carried out under COSHH. Eye protection and FFP 2 respirator to be worn as a minimum. | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK