| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Excavation Work |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Excavation work | Collapse of excavation | Civils operatives, other contractors, visitors | M | Methods of support to be agreed prior to work commencing. Shoring materials to be on site prior to work commencing If shoring is not to be used then sides of excavation must be battered or stepped. Only experienced/trained operative to carry out excavation work. | L |
|  | Underground Services | Civils operatives, other contractors, visitors | M | Service drawings to be on site. Services to be located and exposed by hand as per “Underground Services”. | L |
|  | Falls of plant/materials into excavation | Civils operatives, other contractors, | M | Stop blocks to be used where necessary. Guards rails or protruding boxes (min 1m above ground level) to be in place on all excavations over 2m deep. Excavated material to be stockpiled a minimum of 1.5 m from edge of excavation to avoid surcharging. | L |
|  | Oxygen deficiency/toxic/flammable gases | Civils operatives, other contractors, | M | Gas detectors to be used on all excavations over 2m deep. Excavation to be kept well ventilated. Deeper excavations to have specific rescue plan in place prior to work commencing. Confined space training for deep excavations. | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK