| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Use of Excavators |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Excavation work | Overturning | Plant operators, Civils operatives, other contractors, visitors | M | Safe working load not to be exceeded Operator to have CPCS certification Avoid working on excessive gradients Avoid undercutting or overhangs on excavated faces | L |
|  | Dropping of loads onto personnel | Plant operators, Civils operatives, other contractors, visitors | M | Buckets, loaded or not loaded, shall not to be slewed over personnel Additional training for users of quick-hitch buckets | L |
|  | Detachment of bucket | Plant operators, Civils operatives, other contractors, visitors | M | All excavators have fully automatic quick hitches that fail to safe. All operators have training on quick hitch operation. | L |
|  | Crushing of operative by machine or bucket | Plant operators, Civils operatives, other contractors, visitors | M | Exclusion area to be established around excavator’s working area. Operatives to have method statement briefing prior to staring work. A 360 vision assessment to be undertaken, additional mirrors or camera may be required to permit full vision around vehicle. | L |
|  | Condition of vehicle | Plant operators, Civils operatives, other contractors, visitors | H | Ensure thorough examination certificates accompany machine and a weekly inspection is undertaken by the operator. | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |
|  | Interaction with public/traffic | Members of the public and traffic | M | Flashing beacons to be switched on at all times. | L |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK