| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Labouring Duties |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Manual handling | Sprains/strains Cuts/grazes | Labourers | M | Labourer to lift only objects that are within their acceptable capabilities on site supervision and instruction by site foreman | L |
| General site work | Airborne dust and fumes (Inhalation, allergic response, asphyxiation) | Labourers | M | Personal Protective Equipment (e.g. face mask following assessment) Dangers of airborne dust and fumes explained Assess suitability for young persons with allergic conditions Supervision by site foreman | L |
| General site work | Noise (damage to hearing) | Labourers | M | Ear protection provided as appropriate Warning notices and the use of ear defenders explained to young person Supervision by site foreman | L |
| General site work | Use of power tools | Labourers | H | Labourer is only allowed to operate any power tools (e.g. Stihl saws) that he has been authorised to operate. | L |
| General site work | Trailing cables, uneven ground, adverse weather (slips, trips and falls) | Labourers | M | 1. Instruction given on safe working practice including no running and wearing appropriate footwear 2. Labourer to report any slip and trips risk. Supervision at by site foreman | L |
| General site work | Site traffic | Labourers | M | High visibility clothing. Labourer to walk on pedestrian walkways 100% Supervision at all times by site foreman | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK