LIFTING PLAN FOR DELIVERY OF SITE CABINS AND CONTAINERS

| Site |  | Date |  |
| --- | --- | --- | --- |
| Site/location |  |
| Contract Number |  | Issued by |  |
| Appointed Person carrying out the Assessment: |  | Date of Assessment: |
| Contact: |  | Phone: |  | Fax: |  |
| Site contact: |  | Phone: |  | Fax: |  |
| Description of lift: |
| Details of Cabins |  |
| Weight: |  |
| Dimensions: |  |
| Height of lift (worst case only): |  |
| Max. radius (worst case only): |  |
| Cabin type: |  |
| Details of Lorry mounted Hiab |  |
| Make & model: |  |
| Capacity (SWL at maximum reach): |  |
| Jib length: |  |
| Outrigger spread: |  |
| 12 month test certificate for Hiab (expiry date to be noted) |  |
| Lifting Accessories | 6 month test certificate (Y/N) | Expiry date |
| Slings (chains): |  |  |
| Webbing slings: |  |  |
| Shackles: |  |  |
| Other Accessories: |  |  |
| Ground Conditions (Visual assessment) |
| Access/Egress for lorry |  |
| Lifting position: |  |
| Operator Name | CPCS card registration No: | Expiry date | Category: A36 Lorry loader (hook) Y/N |

Notes

Identification of Hazards

| Proximity Hazard | Present? |  | Proximity Hazard (cont.) | Present? |
| --- | --- | --- | --- | --- |
| Overhead power lines |  |  | Other hazards identified |  |
| Other overhead obstacles |  |  |  |  |
| Underground services |  |  |  |  |
| Excavations |  |  |  |  |
| Unstable/ Soft ground |  |  |  |  |
| Hazardous chemicals/materials |  |  |  |  |
| Confined working area |  |  |  |  |
| Restricted access - width |  |  |  |  |
| Restricted access - height |  |  |  |  |
| Other vehicles |  |  |  |  |

## Assessment of Risk

| Hazard Present | Risk | Action to Avoid or Reduce Risk |
| --- | --- | --- |
| Operational Requirements: |
| Site Provisions: |

# Method Statement

## Lifting Accessories

The lifting accessories, as detailed previously, will be provided by ……………………………… complete with all statutory documentation.

## Weather Conditions

The Appointed Person or, in his absence, Site Manager, will ensure that the lifting operation only takes place if the weather conditions are suitable for the lift.

Ground Conditions

The lorry must be set up on the road surface. Mats must be used under outrigger feet at all times.

Any lifts that require the lorry to be set up off the road must be assessed individually by The Appointed Person and a specific lifting plan produced before any lifting commences.

Attachment/detachment of chain slings to cabin

Slings must be attached from ground level wherever possible. Should the need arise for persons to stand on top of the cabins, then suitable fall protection must be in place (i.e. fall restraint lanyard and harness or similar).

Offloading of cabins

The operator must use the controls on the side opposite where the cabin is to be sited to avoid the risk of the cabin swinging around and crushing them. A competent banksman/signaller may have to be used to aid the operator when off loading.

## Sequence of Operations

| Appointed Person’s Acceptance of Responsibilities |
| --- |
| I confirm that the lifts have been planned and will be carried out in accordance with current legislation and British Standard 7121 and that I accept responsibility for the preparation of this Risk Assessment and Method Statement. | Signed: | Date: |

| Crane Supervisor’s Acceptance of Duties |
| --- |
| I confirm that I have been fully briefed on the contents of this Risk Assessment and Method Statement and that I accept the duty of ensuring that the lift(s) will be carried out in accordance with the method and procedures set out in this document. | Signed: | Date: |

# Text boxes

Notes

Drawings/Plan

- To include location of lorry and proposed site of cabins with distances indicated in metres

- Hazards identified on the previous page to be clearly marked on drawing