| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Use of non-powered hand tools. |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Hand tools | Injury from the tool or material displaced by the use of the tool, e.g. wire brush bristles. | Operator, other workers, client’s personnel, general public, visitors. | H | Wearing eye protection, consider visors. Rubber sleeved chisels. Gloves. Adequate space between workers. Maintenance of the tool and replacements available when damaged. | L |
|  | Work related upper limb disorders. | Operator, other workers, client’s personnel, general public, | H | Ergonomic design of task, e.g. special tools. Good lighting. Job rotation. Good quality access equipment Offsite fabrication where possible. | L |
|  | Dust. | Operator, other workers, client’s personnel, general public visitors. | H | Use vacuum cleaner instead of sweeping, provide hoses and extraction units, wear masks and goggles in accordance with any assessment carried out under COSHH. Forced air ventilation. Wear a respirator usually FFP2 | L |
|  | Falls while using the tool or fall of the tool. | Operator, other workers, client’s personnel, general public,, visitors. | H | Selection of work platform such as scaffolding or MEWP in preference to steps and ladders. \exclusion zone or use of a retractable lanyard for securing the tool to the tool belt. | L |
|  | Fire/explosion/electrocution. | Operator, other workers, client’s personnel, general public, visitors. | M | Carry out specialist risk assessment. | L |
|  | Noise. | Operator, other workers, client’s personnel, general public, visitors. | M | Wearing of hearing protection when above 85dB(A) | L |
|  | Weather. | Operator, other workers, client’s personnel, general public, visitors. | M | Wet weather gear or weather resistant shelters. | L |
|  | Ergonomics. | Operator, other workers, client’s personnel, general public, visitors. | M | Selection of the best tool for the task. Powered tools used where reasonably practicable. Offsite fabrication where feasible. | L |
|  | Unauthorised use. | Operator, other workers, client’s personnel, general public, visitors. | M | Lock away hand tools when not in use. | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK