| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Use of 1 Tonne Hi-Tip Dumper |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Operation of dumper | Overturning | Plant operators, Civils operatives, other contractors, visitors | H | Do not travel on dumper with skip raised Safe working load not to be exceeded (1000kg) Operator to have CPCS certification Ensure ground conditions are suitable Avoid erratic steering or sudden breaking Do not operate on excessive gradients, check manufacturers Info (example...... Terex 1 tonne Hi Tip 4WD Dumper, max Slope gradient 1 in 5 or 20%) ROPS to be fitted and seatbelts worn at all times Check tyre pressures conform to manufacturers guidelines as part of daily checks. | L |
| Operation of dumper | Load dropping off skip | Plant operators, Civils operatives, other contractors, visitors | M | Loads must be levelled off and not heaped Driver must have clear forward field of vision at all times and must not be obstructed by load. (skip kept fully down when mobile). 3. PPE to include Safety helmet, boots, gloves and light eye Protection. | L |
| Operation of Dumper | Operator thrown from vehicle | Plant operators | M | Operator to have CPCS certification Drive at appropriate speeds for site conditions Wear seat belt at all times | L |
| Operation of dumper | Collision with pedestrians/other vehicles | Plant operators, Civils operatives, other contractors, visitors | M | Operator to have CPCS certification Operator to have appropriate driving licence to drive on public roads Site/road speed limits to be adhered to at all times Flashing beacons to be switched on at all times. Hi-vis vests mandatory PPE on site | L |
|  | Unauthorised use | Plant operators, Civils operatives, other contractors, visitors | M | When not in use, dumper must be parked with handbrake applied and keys removed in site compound or other secure area | L |
| Loading of dumper | Injury to operative by machine bucket or load falling | Plant operators, Civils operatives, other contractors, visitors | M | 1. Operators must dismount and turn off dumper during loading operations and stand well clear of loading area. 2. Load only on level ground with the parking break applied 3. Wear light eye protection when driving dumper if risk of load causing eye problems (i.e. airborne dust or grit) | L |

| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |
| --- | --- | --- | --- | --- | --- |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK