NORTHERN COUNTIES SAFETY GROUP LIMITED

Safety Training & Services to the Construction Industry

Only trained and authorised employees to use this machine as per ACOP L114

Safe Use Procedures

Use this machine to produce moulded straight and moulded shaped components

- Correctly use fences, jigs and other protective devices where required

- Feed material into the cutter against the rotation of the cutter

- Report any machinery defects immediately to your supervisor

- Use support tables when feeding long workpiece lengths

- Do not leave the machine unattended whilst the cutter(s) is in motion or running down

- Where possible, use chip limitation cutters

- Always use the braking device to stop the machine/cutters

- Ensure the working area on and around the machine is kept clear at all times

- Use all Personal Protective Equipment (PPE) provided by your employer (e.g. hearing defenders etc)

- Ensure safe Manual Handling techniques at all times

- Make sure dust extraction equipment is fitted and working

Machine Maintenance and Cleaning

- Do not remove off-cuts, clean the machine or adjust guards whilst the auger/chisel is in motion

- Maintain the machine in accordance with the manufacturer’s instructions

- Avoid blowing down the machine or workpiece to remove dust. Use a vacuum cleaner instead

# Text boxes

Safe Use of High Speed Router