| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Use of ladders |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Use of ladders | Falling from height | Operative, 3rd parties | H | Ladder work should be of short duration (e.g. 30 minutes) Work should not involve over reaching. Operative trained in use of ladders and ladder used in accordance with training methods Ladder in good order, visually inspected before use, with current inspection status (normally 6 month thorough inspection tag displayed) Only simple work of a short time duration should be carried out from a ladder. Extra care should be taken when using ladders in occupied areas Do not leave erected ladders unattended Only Class 1 Industrial or BS EN 131 ladders to be used. | L |
|  | Items falling from height | Operative, 3rd parties | H | Use can hooks The method of raising tools and materials should leave hands free Tool belts should preferably be used when working off ladders If using tools that require both hands to operate then a Ladderfix Ladder belt or similar must be used by a trained operative. Barrier off working area if possible | L |
|  | Electric cables | Operative | H | Check route before moving ladder and stop if cables identified | L |
|  | Slips/trips/falls | Operative, 3rd parties | M | Check route before moving ladder and ensure clear walkway | L |

|  | Ladder sliding or slipping | Operative, 3rd parties | H | The ladder should be used in accordance with training methods The ladder should be set firmly and level o the ground Secure the ladder at the top or base to prevent movement by use of Ladderfix Safety Devices or similar where appropriate and ONLY if you are trained to do so.. The correct angle of rest for a ladder, ie 75 degrees or a base to height ratio of 1:4 should be employed | L |
| --- | --- | --- | --- | --- | --- |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK