| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Loading out of bricks, blocks and mortar |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Loading out bricks/blocks/mortar | Repetitive handling Strains/sprains | Operatives carrying out the work, other contractors | M | Bricks/blocks to be mechanically handled (JCB/tele-handler) as close to area where they are to be laid as possible, to minimise distances carried by hand (i.e. loading bay). Bricks/blocks to be carried using wheelbarrows/pallet trucks where possible, to area where they are to be laid. Correct kinetic lifting techniques to be used by experienced operatives who have had manual handling training. 4. Loads are to be broken down to reduce the likelihood of manual handling injuries. | L |
| Loading out bricks/blocks/mortar | Cuts/abrasions to hands | Operatives carrying out the work | M | Wearing of abrasion resistant, latex coated grip gloves. Appropriate Manual Handling aids/equipment to be identified prior to work commencing | L |
| Loading out bricks/blocks/mortar | Existing health issues (back injuries etc) Recurrence of previous injuries | Operatives carrying out the work | M | Check that operatives do not have existing injuries that may be aggravated by the task. Rotate work duties to reduce the risk of Manual Handling injuries. Appropriate Manual Handling aids/equipment to be identified prior to work commencing Ensure that all injuries are reported through the appropriate channels to ensure appropriate logging of health issues. | L |
| Loading out bricks/blocks/mortar | Slips/trips/falls | Operatives carrying out the work | M | Areas to be level and free from obstructions Scaffold working platforms to be kept free from obstructions and tidy | L |

| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |
| --- | --- | --- | --- | --- | --- |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK