| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Confined space entry into manholes. |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Entry into manhole | Explosive atmosphere/oxygen deficiency/toxic gases | Entry Personnel | H | Do not enter manhole unless absolutely necessary and entry is justified. Only trained operatives to enter into confined space Atmosphere to be tested prior to entry. No sources of ignition may require intrinsically safe equipment Manhole to be ventilated using fans or opening other manholes up and down stream if necessary. Open neighbouring manholes to permit airflow Atmosphere to be monitored constantly using triple gas detector at all times. If required for deeper manholes, or if traversing, a 10 minute escape set should be carried by all operatives in the manhole. | L |
| Entry into manhole | Ingress of water/sewage/Weils disease | Entry Personnel | H | Spade off any pipelines that may permit water or flowing solids entry In live sewers over-pumping may be required. Stand-by pump to be on hand to cover breakdowns. Weils disease see separate risk assessment covering hygiene and inoculation | L |
| Entry into manhole | Falls | Entry Personnel | H | Develop full rescue plan and ensure there are adequate numbers of personnel available and who are instructed on plan Full rescue, tripod /fall arrest harness to be used. Tripod with fall arrest winch and rescue winch to be used. Top man to be in place at all times to winch up operatives if necessary and raise the alarm in the event of an emergency. | L |

| Open manholes | Falls into open manholes | Entry Personnel, Operatives, Visitors | M | Open Excavation and manholes to be barriered to prevent access by non-employees. | L |
| --- | --- | --- | --- | --- | --- |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK