NORTHERN COUNTIES SAFETY GROUP LIMITED

Safety Training & Services to the Construction Industry

Only trained and authorised employees to use this machine as per ACOP L114

Safe Use Procedures

This machine is designed to cross-cut material to length, cut angles and compound angles.

- Fit and properly secure guards and safety devices before starting the machine

- Ensure the front extension (finger) guard is kept adjusted as close as possible to the workpiece and within 5mm

- Use a Cross-Cut saw blade of the correct diameter. Avoid ripping on the cross-cut machine

- Keep hands out of danger area and away from the path of the saw blade

- Report any faults with the machine to your supervisor immediately

- Do not leave the machine unattended whilst the saw blade is in motion

- Always use the braking device (if fitted) to stop the machine/blade

- Ensure the working area around the machine is kept clear at all times

- Use all Personal Protective Equipment (PPE) provided by your employer (e.g. hearing defenders etc)

- Ensure safe Manual Handling techniques at all times

- Ensure effective dust extraction is used when operating the machine

Machine Maintenance and Cleaning

- Do not remove off-cuts, clean the machine or adjust guards whilst the blade is in motion

- Maintain the machine in accordance with the manufacturer’s instructions

- Check the saw unit return device pulls the saw blade to the rear of the table fence

# Text boxes

Safe Use of Manual Pull-Over Cross-Cut Saws